## Slide 1
Incompressible Flow over Airfoils
INCOMPRESSIBLE FLOW OVER AIRFOILS

## Slide 2
Incompressible Flow over Airfoils
WHAT IS AN AIRFOIL?
Consider a wing as shown in the figure.
  The wing extends in the y direction
  The freestream velocity is parallel to xz plane
Any section of the wing cut by a plane parallel to the xz plane is called an airfoil.
y
z
x
V∞
Airfoil Section

## Slide 3
Incompressible Flow over Airfoils
WHAT IS AN AIRFOIL?

## Slide 4
Incompressible Flow over Airfoils
EVOLUTION OF AIRFOILS

## Slide 5
Incompressible Flow over Airfoils
EVOLUTION OF AIRFOILS
Early Designs - Designers mistakenly believed that these airfoils with sharp leading edges will have low drag. In practice, they stalled quickly, and generated considerable drag.

## Slide 6
Incompressible Flow over Airfoils
AIRFOIL NOMENCLATURE
Chord c
Leading edge
Thickness
Camber
Mean camber line
Trailing edge

## Slide 7
Incompressible Flow over Airfoils
AIRFOIL GEOMETRY
Airfoil geometry is often characterized by a few parameters such as:
  Maximum thickness
  Maximum camber
  Position of max thickness
  Position of max camber
  Nose radius.
One can generate a reasonable airfoil section given these parameters.

## Slide 8
Incompressible Flow over Airfoils
NACA AIRFOILS
The NACA identified different airfoil shapes with a logical numbering system.
The primary reference volume for all the NACA subsonic airfoil studies remains:
Abbott, I.H., and Von Doenhoff, A.E., “Theory of Wing Sections”, Dover, 1959.

## Slide 9
Incompressible Flow over Airfoils
THE NACA FOUR-DIGIT AIRFOIL
The first family of NACA airfoils, developed in the 1930s, was the “four-digit” series.
The numbering system for these airfoils is defined by:
NACA MPXX
Where:
M is the maximum camber in hundredths of chord.
P is the location of the maximum camber in tenths of the chord.
XX is the maximum thickness, t/c, in percent chord.

## Slide 10
Incompressible Flow over Airfoils
THE NACA FOUR-DIGIT AIRFOIL - EXAMPLE
NACA 2415
The maximum camber is 0.02c
Maximum camber is located at 0.4c from the leading edge.
The maximum thickness is 0.15c

## Slide 11
Incompressible Flow over Airfoils
THE NACA FIVE-DIGIT AIRFOIL
This airfoil is an extension of the 4 digit series. The
numbering system for these airfoils is defined by:
NACA LMMXX
Where:
L: is the amount of camber; the design lift coefficient is 3L/2, in tenths
MM: the location of maximum camber along the chord from the leading edge is MM/2, in hundredths of the chord
XX: is the maximum thickness, t/c, in percent chord.

## Slide 12
Incompressible Flow over Airfoils
THE NACA FIVE-DIGIT AIRFOIL - EXAMPLE
NACA 23012
12% thick airfoil,
The design lift coefficient is 0.3,
The position of max camber is located at x/c = 0.15,
The “standard” 5 digit foil camber line is used.

## Slide 13
Incompressible Flow over Airfoils
THE NACA 6-SERIES LAMINAR FLOW AIRFOIL
One of the most widely used family of NACA airfoils is the “6-series” laminar flow airfoils, developed during World War II.
AB,C-DEE
Where:
A: Is the series designation. B: Location of minimum pressure in tenth of chord from the leading edge (for the basic symmetric thickness distribution at zero lift)
C: The range of lift coefficient in tenth above and below the design lift coefficient in which favourable pressure gradients exist on both surfaces
D: The design lift coefficient in tenth
EE: the maximum thickness in hundredths of chord
After the six-series sections, airfoil design became much more specialized for the particular application.

## Slide 14
Incompressible Flow over Airfoils
THE NACA 6-SERIES LAMINAR FLOW AIRFOIL - EXAMPLE
NACA 65,3-218
6 is the series designation.
The maximum pressure occurs at 0.5c for the basic symmetric thickness distribution at zero lift.
The range of lift coefficient above and below the design lift coefficient in which favourable pressure gradients exist on both surfaces is 0.3
The design lift coefficient is 0.2.
The airfoil is 18 percent thick.

## Slide 15
Incompressible Flow over Airfoils
LIFT GENERATION
Generation of lift by
an airfoil is due to the
imbalance of pressure
distribution over top
and bottom surfaces.

## Slide 16
Incompressible Flow over Airfoils
LIFT GENERATION
If pressure on top is
lower than pressure on
bottom surface, lift is
generated.

## Slide 17
Incompressible Flow over Airfoils
LIFT GENERATION
Flow velocity over the
top of airfoil is faster
than over bottom
surface.

## Slide 18
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
The lift coefficient of an airfoil changes as the Angle-of-Attack changes.

## Slide 19
At low-to-moderate angles
of attack, cl varies linearly
with α.
The slope of this straight line
is called the lift slope.
In this region, the flow moves smoothly over the airfoil and is attached over most of the surface.
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
LOW-TO-MODERATE ANGLES OF ATTACK

## Slide 20
As α becomes large, the flow
tends to separate from the
top surface of the airfoil.
The consequance of this
separated flow at high α is a precipitous decrease in lift and a large increase in drag.
Under such conditions, the airfoil is said to be stalled.
The maximum value of cl, which occurs just prior to the stall, is denoted by cl,max.
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
HIGHT ANGLES OF ATTACK

## Slide 21
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK

## Slide 22
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK

## Slide 23
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=2 deg)

## Slide 24
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=3 deg)

## Slide 25
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=6 deg)

## Slide 26
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=9 deg)

## Slide 27
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=12 deg)

## Slide 28
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=20 deg)

## Slide 29
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=60 deg)

## Slide 30
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=90 deg)

## Slide 31
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=90 deg)
Low a

## Slide 32
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=90 deg)
Moderate a

## Slide 33
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
(α=90 deg)
High a

## Slide 34
cl,max determines the stalling speed
of an airplane. The higher is cl,max
the lower is the stalling speed.
The value of α when lift equals
zero is called the “zero-lift angle
of attack” (αL=0).
Incompressible Flow over Airfoils
VARIATION OF LIFT WITH ANGLE OF ATTACK
At negative α airfoil will have zero lift

## Slide 35
Incompressible Flow over Airfoils
EFFECT OF REYNOLD NUMBER
The lift slope is not
influenced by Re.
cl,max is dependent upon
Re.
The moment coefficient
is insensitive to Re except
At large α.

## Slide 36
Incompressible Flow over Airfoils
EFFECT OF REYNOLD NUMBER
The sum of skin
friction drag and
pressure drag yields the
profile drag.
Profile drag coefficient
is sensitive to Re.

## Slide 37
Incompressible Flow over Airfoils
EXAMPLE

## Slide 38
Incompressible Flow over Airfoils
EXAMPLE (CONT.)

## Slide 39
Incompressible Flow over Airfoils
EXAMPLE (CONT.)
To obtain the drag per unit span, we must use the data diagram.
Since cd = f(Re), let us calculate Re. At standard sea level, μ = 1.789 x 1 0-5 kg/(m.s). Hence,